## Slide 1
Shuyi S. Chen, Mark Donelan, Milan Curcic, Chiaying Lee
RSMAS/University of Miami
Sue Chen, James Doyle, Saša Gaberšek, Shouping Wang
Naval Research Laboratory, Monterey
Rick Allard, Tim Campbell, and Travis Smith
Naval Research Laboratory, Stennis
John Michalakes, National Renewal Energy Lab
Ralph Foster, APL/University of Washington
A Unified Air-Sea Interface for Fully Coupled Atmosphere-Wave-Ocean Models for
Improving Intensity Prediction of Tropical Cyclones
(NOPP Review, Miami, 1 March 2012)

## Slide 2
The goals of this PI team are to:
understand the physical processes that control the air-sea interaction and their impacts on rapid intensity changes in tropical cyclones
develop a physically based and computationally efficient coupling at the air-sea interface for use in a multi-model system that can transition to the next generation of research and operational coupled atmosphere-wave-ocean-land models.

## Slide 3
Outline:
Why UNIFIED air-sea interface module?
Design and Implementation of the unified air-sea interface module (Tim Campbell)
Coupled Atmosphere-Wave-Ocean Model Forecasts of Tropical Cyclones (Sue Chen, Travis Smith)
Evaluation/Verification of Coupled Model Forecasts Using Coupled Air-Sea Observations
Summary

## Slide 4
Atmosphere Model
Ocean Model
Lower boundary conditions (SST, roughness, etc.)
Ocean surface layer
Atmosphere surface layer
Surface forcing (wind, rad./latent/sensible fluxes, etc.)
Uncoupled Models

## Slide 5
Cd
Ck
ARW

## Slide 6
AHW TC
Donelan Cd+ Garret Ck
Charnock

## Slide 7
Latent heat flux
Sensible heat flux

## Slide 8
~2000 W m-2
HWRF experiments (Ligia Bernardet)

## Slide 10
Atmosphere Model
Ocean Model
Surface boundary conditions
Ocean surface layer
Atmosphere surface layer
Air-Sea Interface Module
Ocean surface layer
Interface (waves)
Atmosphere surface layer

## Slide 11
ATMOSPHERE MODEL
OCEAN MODEL
WAVE MODEL
Ua, Ta, mspray, SST, SSH, SSC
twx, twy, SWH, C, spectra (k,q),
wave dissipation
1) Common exchange grid and coupling control
2) Calculation of air-sea interface physics:
(tax, tay) = (twx, twy)+(ttx, tty)+(t)|sea spray ,
(tcx, tcy) = wave dissipation
SH and LH fluxes
spray/bubble generation and effects on momentum, SH, LH fluxes, etc.
tax, tay, SH, LH, SST
u, v, Ta, qa, p, Qrad, rain
tcx, tcy, Qrad, rain
SST, SSH, SSC
Unified Air-Sea Interface Module
Notes: SH, LH = sensible and latent heat fluxes
SST, SSH, SSC = sea surface temperature, height, and current
Tx,ya,c,w, = stress vector (air, current, wave)
Qrad = radiative flux
Mspray = spray mediated momentum
p, qa, Ta = surface presure, water vapor mixing ratio, air temperature

## Slide 12
ESMF Based Software Architecture
Ocean
internal nested grids
ocean exchange grid
ESMF interface
Atmos
internal nested grids
atmos exchange grid
ESMF interface
Wave
internal nested grids
wave exchange grid
ESMF interface
AirSea
ESMF interface
wave field module
sea spray module
surface flux module
Regrid/Interpolation
Redistribution
Parallel Computing
Synchronization and Control
Earth System Modeling Framework

## Slide 13: Architecture of ESMF
ESMF provides a superstructure for assembling geophysical components into applications.
ESMF provides an infrastructure that modelers use to
  Generate and apply interpolation weights
  Handle metadata, time management, data I/O and communications, and other functions
  Access third party libraries
ESMF components have standard methods with simple interfaces.
Low Level Utilities
Fields and Grids Layer
Model Layer
Components Layer
Gridded Components
Coupler Components
ESMF Infrastructure
User Code
ESMF Superstructure
MPI, NetCDF, …
External Libraries
ESMF extends from the lowest level of data representation and parallelism, to higher level model abstraction, geophysical constructions, and Earth System Modeling in general.
Notes: Components in ESMF
There are two types of components in ESMF, Gridded Components and Coupler Components. Gridded Components (ESMF_GridComp) represent the scientific and computational functions in a model, and Coupler Components (ESMF_CplComp) contain the operations necessary to transform and transfer data between them. Both Gridded and Coupler Components are implemented in the Fortran interface as derived types with associated modules. ESMF itself does not currently contain prefabricated Gridded or Coupler Components - the user must write them. The ESMF documentation and source distribution provide tools and examples to guide users through this task.
Each major physical domain in an earth system model is represented as an ESMF Gridded Component with a standardized calling interface and arguments. Physical processes or computational elements, such as radiative processes or I/O, may also be represented as Gridded Components. ESMF Components can be nested, so that parent components can contain child components with progressively more specialized processes or refined grids.
As a model steps forward in time, the physical domains represented by Gridded Components must periodically transfer interfacial fluxes. The operations necessary to couple Gridded Components together may involve data redistribution, spectral or grid transformations, time averaging, and/or unit conversions. In ESMF, a Coupler Component encapsulates these interactions. Coupler Components share the same standard interfaces and arguments as Gridded Components. The key data structure in these interfaces is the ESMF_State object, which holds the data to be transferred between components.
Each Gridded Component is associated with an import State, containing the data required for it to run, and an export State, containing the data it produces. Coupler Components arrange and execute the transfer of data from the export States of producer Gridded Components into the import States of consumer Gridded Components. The same Gridded Component can be a producer or consumer at different times during model execution.
There is no single, generic Coupler Component for all ESMF applications. Modelers write Coupler Component internals using ESMF classes bundled with the framework. These classes include methods for time advancement, data redistribution, calculation of interpolation weights, application of interpolation weights via a sparse matrix multiply, and other common functions.
Coupler Components can be written to transform data between a pair of Gridded Components, or a single Coupler Component can couple more than two Gridded Components. Multiple couplers may be included in a single modeling application. This is a natural strategy when the application is structured as a hierarchy of components. Each level in the hierarchy usually has its own set of Coupler Components.

## Slide 14: From Component Based Architecture to Interoperability
ESMF component interfaces alone do not guarantee technical interoperability – ESMF can be implemented in multiple ways
Also need:
  A common physical architecture – the scope and relationships of physical components
  Metadata conventions and usage conventions
  The next steps for modeling infrastructure involve encoding these conventions in software tools and templates
NUOPC is developing a standard implementation of ESMF across NASA, NOAA, Navy, Air Force and other modeling applications
NUOPC Layer adoption in NEMS, COAMPS, & NAVGEM
Notes: Interoperability of modeling components can be implemented at a range of different levels. ESMF interfaces enable model components to be called in a standard way, but they do not guarantee that modeling components of the same type (ocean models, for example) can be replaced without further code changes. A key goal for the next five years is to increase the level of interoperability so that fewer code changes are required when model components are exchanged or introduced.
This requires action along several fronts. One is promoting a common physical architecture, which defines the scope of components and how they are connected (for example, whether surface processes are handled as a sub-process of the atmosphere). Another is identifying common pieces of code and metadata, standardizing them, and refactoring them into templates that can be reused by multiple groups. Lastly, coupling mechanisms must be structured so that they can be composed and reconfigured more easily, and so that compatibility checking can be automated. These strategies promote a healthy balance between the flexibility needed for research and the constraints required for streamlined operations.
Collectively, these strategies are referred to as “common model architecture” (CMA) by the National Unified Operational Prediction Capability (NUOPC), a consortium of Navy, Air Force and NOAA environmental prediction centers.
The NUOPC Content Standards Committee and ESMF Core Team are working towards a common model architecture through the design and implementation of a NUOPC interoperability software layer.

## Slide 15: Building an Information & Interoperability Software Layer
Applications of information layer
Native model data structures
Parallel generation and application of interpolation weights
Run-time compliance checking of metadata and time behavior
Fast parallel I/O
Redistribution and other parallel communications
Automated documentation of models and simulations
Ability to run components in workflows and as web services
Structured model information stored in ESMF wrappers
User data is referenced or copied into ESMF structures
modules
fields
grids
timekeeping
Standard data structures
Standard metadata
Field
Grid
Clock
Component
Attributes: CF conventions, ISO standards, METAFOR Common Information Model
ESMF
NUOPC Layer
Common Model Architecture -- technical rules and associated generic code collection with compliance checking

## Slide 16: Current Implementation in COAMPS Using NUOPC Interoperability Layer
Atmosphere
(internal surface layer)
Ocean
AirSea Interface
Wave
SST,
CHNK
SST
RSTG, SDC, WBC
WIND, MSLP, STRS,
HFLX, MFLX, SWRD
MSLP, STRS, HFLX,
MFLX, SWRD
WIND
SSH, SSC
CHNK
NUOPC Connector
(connect import state to export state; compute regrid and data routing)
NUOPC Model
NUOPC Mediator
All fields defined using NUOPC Field Dictionary

## Slide 17
WRF
HYCOM
UMWM
Ua, Ta, SST, SSH, SSC
twx, twy, SWH, C
wave dissipation
(tax, tay) = (twx, twy)+(ttx, tty),
(tcx, tcy) = wave dissipation
tax, tay, SH, LH, SST
u, v, Ta, qa, p, Qrad
tcx, tcy, Qrad
SST, SSH, SSC
Unified Air-Sea Interface
University of Miami Wave Model (Donelan et al. 2012)
ESMF
Coupled WRF-UMCM-HYCOM
Notes: SH, LH = sensible and latent heat fluxes
SST, SSH, SSC = sea surface temperature, height, and current
Tx,ya,c,w, = stress vector (air, current, wave)
Qrad = radiative flux
Mspray = spray mediated momentum
p, qa, Ta = surface presure, water vapor mixing ratio, air temperature

## Slide 18
Air-Ocean Coupled COAMPS-TC
Homogenous Track Error
Track
Negative intensity bias
Coupled COAMPS-TC has an average (27 samples) negative intensity bias
Higher horizontal resolution may be needed for the coupled COAMPS-TC
Further calibration of new atmospheric physics for 5 km coupled COAMPS-TC is needed
(09L, 12L, 14L, 16L, 17L)

## Slide 19
AXBT Demo Project
Hurricane Irene (2011)
48 H SST difference
3-4 °C hurricane-induced SST cooling along the coastal area
Little impact on track and intensity forecast

## Slide 20
High-Resolution Coupled COAMPS Simulations of Fanapi
Atmosphere: 27, 9, and 3 km
Ocean: 9 and 3 km
Wave: 1/6 degree
Model spin-up from 2010090800
12 h update cycle
3-4 °C cold wake
Intensity overall is good
72 h SST anomaly

## Slide 21
Intensity Comparison
Max Wind
Min SLP

## Slide 22
Intensity Comparison
Max Wind
Min SLP

## Slide 23
Intensity Comparison
Max Wind
Min SLP

## Slide 24
Intensity Comparison
Total flux
10 m Air Temperature

## Slide 25
Intensity Comparison

## Slide 26
Intensity Comparison
Comparison of PBL schemes

## Slide 27
Asymmetric tangential wind speed and TC secondary circulations
Inflow
Inflow
outflow
outflow
Storm relative Radial wind speed
South
Deep inflow layer on the south side
North
Storm relative tangential wind speed
ITOP Dropsonde Analysis
Near Fanapi Eye

## Slide 28
CWRF forecast of tangential and radial winds in Fanapi

## Slide 29
ITOP Dropsonde Analysis
Near Fanapi Eye
uncoupled
Coupled
Dropsonde
COAMPS-TC

## Slide 30
CWRF: Uncoupled
CWRF: Coupled
PBL model has difficulty with stable stratification

## Slide 31
00 UTC Sep 18
18UTC Sep 17, 2010 AXBT 307 mission
ITOP AXBT Analysis
Co-located observations

## Slide 32
Cold wake 1
XBT 4 & 45: (27.06-25.58)/4.7333 hr
Cooling rate = 8.68e-5°C/s, 1.48°C total cooling
XBT 4: Sep 17, 2205 UTC
XBT 45: Sep 18, 0249
Cold wake 2
XBT10 & 29: (28.29-27.6)/2.2hr
Cooling rate = 8.7e-5°C/s, 0.69°C total cooling
XBT 10: Sep 17, 2253 UTC
XBT 29: Sep 18, 0105 UTC
SST cools about 0.35°C per hour
Ocean cooling rate can be used to validate the coupled model wind stress forcing
ITOP AXBT Analysis
Co-located observations

## Slide 33
Summary
Air-ocean Coupled COAMPS-TC system was demonstrated real-time in 2011 AXBT demo project in the Atlantic basin
Special AXBT observation had a small impact on the COAMPS intensity and track forecast
A series of Typhoon Fanapi sensitivity runs were conducted to diagnose the Coupled COAMPS-TC low intensity problem associated with the energy input from the ocean and atmospheric PBL mixing
Results show we can improve the coupled COAMPS-TC intensity by using:
  new sea spray
  level-off momentum drag with URI wave age-dependent drag
  a lower value of level-off momentum drag and higher Ck/Cd ratio
  Adjust the mixing length in the PBL

## Slide 34: Ocean-Wave Coupling Overview
Hurricane Ivan (September 2004) was simulated to compare to observational data collected in the Gulf of Mexico (ADCP, wave buoy, Scanning Radar Altimeter (SRA)). Six-way air (COAMPS)/sea (NCOM)/wave (SWAN) coupling in the ESMF framework was utilized.
Recent work at NRL-SSC has focused on the wave source terms and drag coefficient in SWAN to improve wave input and dissipation, and ocean/wave model interactions (e.g. Stokes’ Drift Current (SDC), current interaction in SWAN).
Results show that the improved SWAN physics and ocean/wave coupling provide satisfactory results when compared to in-situ observations.

## Slide 35
COAMPS (Air/Ocean/Wave Current Configuration)
COAMPS® and COAMPS-OS® are registered trademarks of the Naval Research Laboratory.
NAVDAS
NCODA
Atmos OBS
NCODA
QC
CAGIPS
NOGAPS
User configurable
6 or 12 hr atm
update cycle
COAMPS®
coupler
NCOM
GOFS
NCODA
Convert
T/S/U/V
Bathy/Clim
BC/IC
NCODAQC
SST, SSH
ICE, PROF
SHIP, GLDR
Ocean OBS
NCOM Setup
ESMF
DATABASE
GDEM MODAS
DBDBV DBDB2
OSUTide Rivers
obs, remote
sensing, text
GLOBE
WVS
Climo
ATMOSPHERE BOUNDARY
CONDITIONS (ANALYSIS)
SWAN/WW3
WAVE Model Setup

## Slide 36: Hurricane Ivan COAMPS-TC Setup
Ivan – Gulf of Mexico (SEP 2004)
Horizontal Resolution:
Atmos: 18, 6, and 2 km (child moving)
Ocean: 4 km
Wave: 8 km
Vertical Resolution:
- 60 atmospheric levels
- 50 ocean levels
Boundary Conditions:
Atmos: 1o NOGAPS
Ocean: Global NCOM
Data Assimilation:
Atmos: NAVDAS (3DVAR)
Ocean: NCODA (3DVAR)
12 hour update cycle for spinup
Observation Data:
ADCP (Bill Teague, NRL)
SRA (Isaac Ginis, URI)
Wave Buoy Data (NOAA)

## Slide 37: SWAN Wave Physics Enhancements
Rogers et al. (2011) introduced observation-based (Donelan et al. (2006))
whitecapping source terms in SWAN based on earlier work by Tsagareli et al.
(2010) and Babanin et al. (2010).
  -- Source terms conform to two features observed in the real ocean reported in
  literature. While classic Komen wave physics in SWAN considers all
  waves breaking at all times, Babanin physics utilizes a two-phase
  dissipation of waves of any particular frequency due to:
  1. Instability (and breaking) of waves of that frequency
  2. Destabilization by larger breaking waves (e.g. through turbulence)
  A threshold is introduced to the wave breaking such that when the
  local spectral density falls below a spectral threshold, no breaking
  occurs at that frequency.
Wind input terms in SWAN are taken directly from observations and modified
  to scale with the friction velocity, u*, and a physical constraint on the total
  stress (drag) included (Hwang, 2011).

## Slide 38
The combined effects of a new wave input and dissipation parameterization in SWAN (Rogers et al. 2011, Babanin et al. 2010) and reduced drag coefficient (Hwang 2011) based on observations in tropical cyclones significantly reduces the SWH in strong TCs such as Hurricane Ivan. Ocean/Wave
coupling induces additional SWH reduction.
COAMPS-TC
Wu
5-6 m difference
Sensitivity tests for Hurricane Ivan
Maximum Intensity
Significant Wave Height
Drag Formulation Sensitivity Evaluations

## Slide 39: Ivan Altimeter Comparison
Uncoupled
(ocean/wave)
Coupled
(ocean/wave)

## Slide 40
Coupled WRF-UMWM-HYCOM: Effects of currents on waves
Wave
Wave+Current
Difference in SWH

## Slide 41: Ivan Altimeter Comparisons Uncoupled vs Coupled
Uncoupled (ocean/wave)
Coupled (ocean/wave)

## Slide 42: Ivan Buoy Comparisons
Buoy 42001
Buoy 42040
~ 2 m
difference
~ 1 m
Although storm translation lag is present, comparisons show that providing
SWAN surface currents from NCOM improves the overall SWH.

## Slide 43: IVAN SRA Wave Validation
SRA flight
SWH (m)
Wave
Prop.
Dir. (deg)
September 14-15, 2004

## Slide 44: Ivan Current Evaluation Coupled (w and w/o Stokes’ drift)
The passing of Stokes’ Drift Current from SWAN to NCOM shows improvement in both the Mean Directional Error (MDE) and current velocity. In an extreme event such as Hurricane Ivan, the SDC can be as much as 10-20% of the total current velocity near the surface.

## Slide 45: IVAN Ocean Current Validation
Forecast Hour (partial time series)
Forecast Hour
Current Velocity (m s-1)
m s-1
Coupled (wave/ocean)
Velocity max: ~ 2.2 m s-1
Current Velocity at 6 m (ADCP M1)
OBS max: 2.1 m s-1
COAMPS max: 2.2 m s-1
0
5
10
15
20
25
30
35
2.5
2.0
1.5
1.0
0.5
0
0 12 24 36 48 60 72
0
50
25
Depth (m)

## Slide 46: SUMMARY
Overall, six-way coupling of Hurricane Ivan with the new SWAN wave physics and wave input schemes produced satisfactory results (SWH, intensity, ocean response) when compared to observations. This is a large improvement over the classic Komen physics and Wu
stress and drag formulation in SWAN.
In addition to the new SWAN wave input and dissipation parameterizations, ocean to wave coupling reduced the SWH in high wind conditions by as much as 1-2 m. Satellite altimeter and buoy observations agreed well with the SWAN SWH.
The Stokes’ Drift Current is very important in extreme wind conditions near the surface. ADCP observations indicate that the SDC component can be approximately 10-20% of the total current velocity.

## Slide 47
Coupled air-sea observations provide an unprecedented data set for understanding of tropical cyclones and coupled model evaluation/verification as well as coupled data assimilation

## Slide 48
Mission | 0620w
Dropsonde | 49
AXBT | 33
Typhoon Fanapi
Warm air flows over cold ocean, downward sensible heat flux
Air Temperature
A
B
Air-sea interface
Ocean Temperature
WARM
WARM
COLD
A
B
Cold air flows over warm ocean, upward sensible heat flux
Notes: Direction of Energy reverses in these two regions

## Slide 49
Stable Boundary Layer: surface is cooler than the air (Stull 1988)
> 0 - stable
= 0 – neutral
< 0 - unstable
qv
z
Stable
Unstable
Neutral
Static stability
Typhoon Fanapi
Obs
CWRF
Notes: From stull, the definition of SBL is when the surface is cooler than the air, The the air-temperature will always adjust toward surface temperature, and therefore there will be a reverse temperature profile as the figure shows here.
This is where the stable boundary layer is.
So one way to form the stable boundary is to cooling the surface for a certain amount of time. Over land, radiation cooling at night could be one cause.
So how about under hurricane circumstance. Hurricane usually form over the warm water as the figure shows here, which his a pre-storm sea-sruface temperature, and here is the storm location.
Over ocean, under this warm environment, the only way for ocean surface to cool down in hurricane is through the air-sea interaction which bring up the colder water underneath and cool the surface.
However, maybe because the lack of observations, and coupled model… we never really understand if there is a stable boundary layer, and what is its impact on storm??

## Slide 50
ITOP: Co-located Dropsondes and AXBTs

## Slide 53
Effect of Sea Spray on Fanapi Simulations
Averaged fluxes within 150 km radius of eye
New sea spray increases more sensible flux
Smaller increase in latent heat flux
Fully coupled run has a 32% less total flux over the ocean compared to the uncoupled run
New sea spray provides about 5% flux increase
With new sea spray, there is still a large flux difference between coupled and uncoupled runs
Sensible
Latent

## Slide 54
Uncoupled WRF
Coupled WRF-HYCOM
Coupled WRF-UMWM-HYCOM
Uncoupled and Coupled Model Forecasts of SH and LH fluxes

## Slide 55: Synthesis On Turbulent Flux Parameterizations: Combined Observations from ESRL, UConn, UMiami
Neutral turbulent transfer coefficients at z=10 m as a function of wind.
Symbols are Direct Data (14,450 observations; 90% between 3 and 17 m/s)
Dash Lines are Parameterizations
*Observations of 3 Research Groups Agree Closely ( with 5%) But Need More High Speed Data
*Spread of Parameterizations is Greater Than Spread of Observations
*NOAA COARE model is the best fit
CD (Donelan et al. 2004)
CK (Jeung et al. 2010)

## Slide 57
Observed and Modeled Structure and Intensity of Fanapi
Notes: Obs 9/16 21z-9/17 03z, WRF 9/17 22z
Obs 9/17 21z-9/18 03z, WRF 9/18 06z

## Slide 58
Coupled WRF-UMCM-HYCOM Simulated SST and TMI satellite observed SST

## Slide 59
Recent Progress and Accomplishment:
Development of the unified air-sea interface module with ESMF/NUOPC with interoperability layer that can be transitioned to NEMS
Coupled model improved TC structure and intensity, ocean and surface waves forecasts
Using coupled observations to evaluate/verify coupled model forecasts
Work to be completed in 2012:
Add ESMF in WW3
Test and evaluate the interface module in multi-model systems: COAMPS-SAWN-NCOM, COAMPS-WW3-NCOM, WRF-UMWM-HYCOM
On-going R2O activity:
COAMPS-TC is running in Stream 2 operation
Coupled model evaluation/verification
Future Work:
Standardized coupled modeling framework that allows researchers to contribute physics and facilitate/accelerate R2O and O2R
Ensemble forecasts using coupled models that can be used for coupled data assimilation and assessment of coupled uncertainties.